## Slide 1: Bridging the Moore’s Law Performance Gap with Innovation Scaling
Todd Austin University of Michigan
Notes: New slides?
- slide on 10 years ago? To gauge our changes?
- slide on “Advice for Pis”
- Work 10 years out, take the risk, the center will support you
- Put your best work in the center, the center will support you
- Collaborate, take the opportunity, it will provide benefits
- Work with (not for) your sponsors, stakeholders can provide excellent insight and support

## Slide 2: Moore’s Law Performance Gap
Today, gap is cresting 10x

## Slide 4: We Investigate: Who’s to Blame?
?

## Slide 5: The Programmer?
Some say programmers cannot overcome hard parallel programming problems
Not the case, as parallel programming techniques and infrastructure is advancing more quickly than ever before
  Map-reduce
  Hadoop
  Spark
  NoSQL databases
  Memcached
  Cassandra

## Slide 6: Largest NA Bitcoin Miner
GPGPU-based system
Fills 2000 sq.ft. warehouse
Computes 1 petahash/s
Reportedly generates $8M in Bitcoins per month
Unfortunately soon to be obsolete as Bitcoin difficulty continues to scale

## Slide 7: The Educator?
Perhaps CS education is failing to educate
Not the case, CS education is booming
  @ Michigan CS enrollments are up nearly 250% from 5 years ago
  Average entrant GPA’s are up as well
Quality of CS education is on an upward trend
  Among the highest ranked educators by students (@ Michigan)
  Young area has less “dead wood” than our more venerable engineering counterparts
  Active-learning approach to education is the norm for CS in the US

## Slide 8: CS Education in Ethiopia
I have been working with Addis Ababa Institute of Technology to develop CS and IT coursework since 2008
Special focus on building infrastructure and developing active learning
Nearly 600 students in the CS program
2nd most popular major in the university
  With many job opportunities
  The first?

## Slide 9: Silicon Technology?
Are transistors failing us, in the past scaling decreased latency, power, cost
Yes in part, silicon scaling has stalled for gate oxide layers
  Due to leakage concerns, gate oxide scaling has stopped
  This leaves threshold voltages high and prevents large decreases in Vdd
Because scaling has become uneven with the transistor
  Dennard scaling has all but stopped
  But, silicon is still bringing more transistors every generation, and will continue for perhaps a decade or so
Ultimately creates the dark silicon dilemma
  Which prevents all of the chip to be active at the same time

## Slide 10: The Dark Silicon Dilemma
Courtesy Michael Taylor @ UCSD

## Slide 11: The Dark Silicon Dilemma
Courtesy Michael Taylor @ UCSD

## Slide 12: The Dark Silicon Dilemma
Courtesy Michael Taylor @ UCSD

## Slide 13: Silicon Technology?
Are transistors failing us, in the past scaling decreased latency, power, cost
Yes in part, silicon scaling has stalled for gate oxide layers
  Due to leakage concerns, gate oxide scaling has stopped
  This leaves threshold voltages high and prevents large decreases in Vdd
Because scaling has become uneven with the transistor
  Dennard scaling has all but stopped
  But, silicon is still bringing more transistors every generation, and will continue for perhaps a decade or so
Ultimately creates the dark silicon dilemma
  Which prevents all of the chip to be active at the same time

## Slide 14: The Architects?
For decades, architects relied on technology scaling to provide for much of the generational design benefits
Can architects bridge the Moore’s law performance gap with innovative designs?
  Perhaps, what provides the 10x+ needed to bridge the gap?
  Initially, many-core was thought to provide a scalable solution
  Many-core designs provide value, but it is not a universal panacea
Architects have other tricks up their sleeves
  Application-specific architectures, in particular

## Slide 15: Example: CryptoManiac Processor
Circuit-level functional unit design tucks pre- and post-Boolean ops into clock cycle
Architecture-level ISA extension exposes pre/post-ops
Application-level programming re-expresses algorithms to leverage optimization
20% performance benefit (could be recast as energy benefit)
CM
Proc
CM
Proc
CM
Proc
Keystore
Req Scheduler
In Q
Out Q
requests
.
.
.
results
Pipelined
32-Bit
MUL
1K Byte
SBOX
Cache
32-Bit
Adder
32-Bit
Rotator
XOR
AND
Logical Unit
XOR
AND
Logical Unit
{tiny}
{short}
{tiny}
{long}
[Austin]

## Slide 16: Example: EFFEX Feature Extraction
Feature Extraction
Object Geometric & Semantic Reasoning
Contextual Scene Reasoning
Local Features, Global Features
Spatial-Temporal Relationships
Typical computer vision pipeline
Object Geometric & Semantic Reasoning
Contextual Scene Reasoning
Feature Extraction
Local Features, Global Features
Spatial-Temporal Relationships
Local Features, Global Features
Image
Preprocess image
Scan image for potential feature locations
Filter feature locations
Generate signature of confirmed features
Post process feature descriptors
Feature Extraction
[Clemons, Austin]

## Slide 17: Example: EFFEX Feature Extraction
Patch Memory
Vector Reduction Units
Heterogeneous Multicore
Initial EFFEX design
  90x greater efficiency for feature extraction algorithms
Notes: If you are reading this note, you are probably awesome. Use the word sliding window here.

## Slide 18: Moving Beyond Homogeneous Parallelism
Many-core designs, while helpful, will soon realize their (perhaps full) potential, what big ideas are next that can translate innovation into scaling
Heterogeneous parallelism is the key to 10-100x energy-efficiency gains in light of slowing silicon
  C-FAR seeks sustained scaling through highly reusable composable customization, and affordable design and manufacturing

## Slide 19: The Policy Makers?
Perhaps, while solutions exist, policy makers do not have the will to support research into solving this problem
Not the case, while all of the engineering sciences have been hit with funding cuts in the last decade
  Computer engineering has faired better than many other engineering sciences
  Investments in CE research are still flowing from industry and goverment
Example: Center for Future Architectures Research (C-FAR)
  27 PIs from 14 US universities
  US$30M investment over 5 years

## Slide 20: C-FAR: Center for Future Architectures Research
Communication
(Margaret Martonosi)
Computation
(David Brooks)
Storage
(Steven Swanson)
Design Themes
Applications-to-Architectures
(Krste Asanovic)
Resilient System Design (Valeria Bertacco)
System Integration (Naveen Verma)
Viability Themes
What solutions are needed?
Will our ideas actually work?
Sponsored by SRC/DARPA
Goal: Innovation-based scaling for 2020-2030’s

## Slide 21: The Blame? Cost of Design
The one idea I want to leave with you today…
Successfully bridging the Moore’s Law Performance Gap is less about “How” to do it, and more about “How Much” does it cost to attempt to do it
My claim: if we can effect a 100x reduction in the cost to bring a design to market, performance challenges will eventually solve themselves as the market flourishes with orders of magnitude more designs, some of which will be the big design wins of tomorrow

## Slide 22: Don’t Believe Me?
Well, you can’t argue with Mother Nature!
  r/K selection theory is a biological mechanism that organisms use to better adapt to their environment
In unstable environments, r-selection predominates as the ability to reproduce quickly is crucial
In stable environments, K-selection predominates as the ability to compete successfully for limited resources is crucial

## Slide 23: Design Costs Are Skyrocketing
Chart: Silicon Technology Node
| 0.5u | 0.35u | 0.25u | 0.18u | 0.13u | 90nm | 65nm | 45nm
Design, Layout, and Verification | 2 | 2.25 | 2.25 | 9 | 13.5 | 18.5 | 33 | 34
Software Development and Test | 0.25 | 0.5 | 1.25 | 4 | 5 | 9 | 13 | 21
Mask Production Costs | 0.25 | 0.25 | 0.5 | 1 | 1.5 | 1.5 | 4 | 5
Source: International Business Strategies
23

## Slide 24: High Costs Kill Innovation
Heterogeneous designs often serve smaller markets

## Slide 25: Outcome: “Nanodiversity” is Dwindling
Chart: Year
| 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009
10000 | 10000 | 10900 | 10990 | 9900 | 9150 | 7970 | 5050 | 3950 | 3780.15 | 3712.1073 | 3623.0167 | 3409.2587 | 3167.2014 | 2866.3172 | 2244.3264
Source: Gartner Group
25

## Slide 26: Silicon Today: The Good, the Bad and the Ugly
The Good: Moore’s law will continue for the near future
  It won’t last forever, but that another problem
The Bad: Dennard scaling has all but stopped, leaving innovation to fill the performance/power scaling gap
  E.g., app-specific design, custom accelerators
The Ugly: Hardware innovation requires design diversity, which is ultimately too expensive to afford
  Skyrocketing NREs will necessitate broadly applicable (vanilla and slow) H/W designs

## Slide 27: The Remedy: Scale Innovation via Lower Design Cost
Ultimate goal: make customized design sufficiently inexpensive that anyone can do it anywhere
  Address all NRE factors: market size, design costs, build costs
  Take inspiration from Web 2.0, and subsequent innovation explosion
Approach #1: Reduce the cost of custom hardware
  With better tools that understand and leverage the benefits of customization
  By embracing open-source hardware design solutions
Approach #2: Widen the applicability of custom hardware
  Increasing market applicability with composable customization mitigates potentially higher NREs
Approach #3: Reduce the cost of manufacturing hardware
  Utilize assembly-time customization to slash the cost of customization
Approach #4: Slash software development costs
  Through more effective reuse, wider adoption of open source technologies, and novel approaches to verification

## Slide 28: 1) Reduce the cost of custom hardware
Better tools
  Scalable accelerator synthesis and compilation, generates code and H/W for highly reusable accelerators for a wide range of applications
  Composable design space exploration, composability permits novel search techniques based on machine learning, enables efficient exploration of highly complex design spaces
Embrace open-source concepts
  Example: Berkeley’s RISC-V architecture
Composed design space
CPU, GPU, Accelerator Design Spaces
automatic composition
MxPA/FCUDA
RTL

## Slide 29: Berkeley’s RISC V Open-Source ISA

## Slide 30: 2) Widen the Applicability of Custom H/W
ESP: Ensembles of Specialized Processors
  Ensembles are algorithmic-specific processors optimized for code “patterns”
  Patterns capture common operations across many applications, each with unique communication and computation structure
  Approach has the promise of custom accelerator speed and efficiency that is widely applicable to general purpose programs
ILP Engine
Dense Engine
Sparse Engine
Graph Engine
ESP Core
Glue Code
Dense Code
Sparse Code
Graph Code
ESP Code
Dense
Graph
Sparse
…
Applications
Multimedia Analysis
Computer Vision
Machine Learning
Computational Patterns
Specializers with custom implementations and autotuning
[Asanovic, Keutzer]

## Slide 31: 3) Reduce the cost of manufacturing H/W
H/W brick
Brick-and-mortar silicon explores assembly-time customization, i.e., MCMs + 3D + FPGA interconnect
Diversity via brick ecosystem & interconnect flexibility
Brick design costs amortized across all designs
Robust interconnect and custom bricks rival ASIC speeds
31
[Bertacco, Carloni, Mercaldi]
Brick-and-mortar silicon
design flow:
Assemble brick layer
Connect with mortar layer
Package assembly
Deploy software

## Slide 32: 4) Slash Software Development Costs
Implement more software reuse
Embrace more fully the open-source movement
Audience, other ideas?

## Slide 33: Conclusions
Heterogeneous design could continue Moore’s law scaling through innovation alone
  But, it requires a diverse hardware ecosystem with affordable customization
Affordable customization won’t happen without our help
  Widen the applicability of customization
  Reduce the cost of customized design
  Reduce the cost of custom manufacturing
Resulting “nanodiversity” is a good thing
  Better perf, power, cost, capability
  More jobs, companies, and students
  More competition and scalable innovation

## Slide 34: Questions
?
?
?
?
?
?
?
?
?
?
?
?